BelgianSmartMeter2Domoticz

---
Goal
Integrate Belgian Sagemcom S211 smart meter in domoticz
Understand P1 port
Limited budget
Hardware cost only
No subscription cost

---
Credits
Code from: https://github.com/jantenhove/P1-Meter-ESP8266
Instructions from:
http://domoticx.com/p1-poort-slimme-meter-data-naar-domoticz-esp8266/
https://www.fluvius.be/sites/fluvius/files/2020-01/dmk-demo-v2.1-rtc.pdf

---
Hardware
LOLIN Wemos D1 Mini
5V
Wireless
ESP8266 architecture
Cheap

---
Get up and running 1 of 2
- Download & install arduino IDE
  https://www.arduino.cc/en/main/software
- Add ESP8266 boards support to Arduino IDE
  - File > Preferences > Additional Boards Manager URL:
    http://arduino.esp8266.com/stable/package_esp8266com_index.json
  - Tools > Boards > Boards Manager:
    install ESP8266 boards
- Install the ESP8266 SoftSerial library from Arduino IDE
  - Sketch > Include Library > Manage Libraries
    I installed AltSoftSerial library from Paul Stoffregen
- Add CRC16.h to a new folder you call CRC16 in your Arduino/Libraries folder.
  E.g. for Linux in /home/yourusername/Arduino/libraries/CRC16/CRC16.h
- Add BelgianSmartMeterToDomoticz.ino to arduino/BelgianSmartMeterToDomoticz/ folder

---
Get up and running 2 of 2
Configure the sketch to connect to your network

---
Testing the setup > Serial monitor
I think if you would power the D1 Mini from both the GPIO pins and through USB, you would see magic smoke.
If you want to see serial monitor output whilst testing, I advise creating a second RJ11/12 cable
²
1. Not Connected
2. 5V**
3. Ground**
4. Not Connected
5. RxD*
6. Not Connected
1
6

---
Example Serial console output
/FLU5\632470339_T
0-0:96.1.4(50213)
0-0:96.1.1(3153414731313030303838303136)
0-0:1.0.0(200912060615S)
1-0:1.8.1(001210.105*kWh)
1-0:1.8.2(002703.013*kWh)
1-0:2.8.1(001750.611*kWh)
1-0:2.8.2(000507.828*kWh)
0-0:96.14.0(0002)
1-0:1.7.0(01.850*kW)
1-0:2.7.0(00.000*kW)
1-0:32.7.0(232.3*V)
1-0:31.7.0(008*A)
0-0:96.3.10(1)
0-0:17.0.0(999.9*kW)
1-0:31.4.0(999*A)
0-0:96.13.0()
0-1:24.1.0(003)
0-1:96.1.1(37464C4F32313139313134373932)
0-1:24.4.0(1)
0-1:24.2.3(200912060501S)(00866.794*m3)
!8CA4
VALID CRC FOUND!
[HTTP] GET... URL: http://192.168.1.4:8080/json.htm?type=command&param=udevice&idx=183&nvalue=0&svalue=1210105;2703013;1750611;507828;1850;0
[HTTP] GET... code: 200

---
Example Serial console output
/FLU5\632470339_T
0-0:96.1.4(50213)
0-0:96.1.1(3153414731313030303838303136)
0-0:1.0.0(200912060615S)
1-0:1.8.1(001210.105*kWh)
1-0:1.8.2(002703.013*kWh)
1-0:2.8.1(001750.611*kWh)
1-0:2.8.2(000507.828*kWh)
0-0:96.14.0(0002)
1-0:1.7.0(01.850*kW)
1-0:2.7.0(00.000*kW)
1-0:32.7.0(232.3*V)
1-0:31.7.0(008*A)
0-0:96.3.10(1)
0-0:17.0.0(999.9*kW)
1-0:31.4.0(999*A)
0-0:96.13.0()
0-1:24.1.0(003)
0-1:96.1.1(37464C4F32313139313134373932)
0-1:24.4.0(1)
0-1:24.2.3(200912060501S)(00866.794*m3)
!8CA4
VALID CRC FOUND!
[HTTP] GET... URL: http://192.168.1.4:8080/json.htm?type=command&param=udevice&idx=183&nvalue=0&svalue=1210105;2703013;1750611;507828;1850;0
[HTTP] GET... code: 200
Example telegram
Always starts with a /
Always ends with line starting with !
Cyclic redundancy check done on the message
Not all information sent to Domoticz

---
Message labels and values
Source: https://www.fluvius.be/sites/fluvius/files/2020-01/dmk-demo-v2.1-rtc.pdf

---
Connecting to the P1 port over RJ12
Powered over RJ12, not USB
²
1. 5V***
2. 5V**
3. Ground**
4. Not Connected
5. RxD*
6. Ground***
1
6
* I used GPIO 2 on the D1 Mini
** When closing this circuit with 5V, this signals the smart meter to start sending data over the RxD pin
*** The Fluvius smart meter provides power over these pins, so you don’t have to power the D1 Mini over a separate USB/power cable

---
Connecting to the P1 port over RJ12
Powered over RJ12, not USB
²
1. 5V***
2. 5V**
3. Ground**
4. Not Connected
5. RxD*
6. Ground***
1
6

---
The arduino code
https://github.com/Raeymeister/BelgianSmartMeter2Domoticz
- Based on Jan Ten Hove’s Github project
- Altered for belgian implementation of DSMR P1 V5.0.2
  - HI/LO production/consumption identification in the telegram is inverted BE vs NL
  - Gas identification is different BE vs NL
  - MAXLINELENGTH extended

---
Conclusion
- €6 to get data from a Fluvius smart meter to Domoticz
- Thanks Jan ten Hove
- Links below
- Let me know what you think